## Slide 1: SCWR Stability Analysis
Won Sik Yang Nuclear Engineering Division
Argonne National Laboratory

## Slide 2: Background
SCWR has large axial variation of coolant density similar to BWR
  It is possible to have instability problems similar to BWR
  Gen-IV roadmap identifies power-flow stability as one of important technology gaps of SCWR
BWR stability issue is no major industry safety concern
  BWRs are designed such that instabilities would not occur under normal operating conditions
  Stability problems may arise during start-up or transients
  Operating instructions contain clear rules to avoid operating power-flow region that may produce power-void oscillations
Notes: The power-flow stability related to thermal-hydraulic and thermal-nuclear coupled instabilities is one of the important technology gaps identified by Gen-IV roadmap, and needs to be investigated thoroughly.

## Slide 3: Events of BWR Core Instabilities
Date | Plant | Country Manufc. | Event (as described by the operator)
30.06.82 | Caorso | IT, AMN | Core instability during plant start up
01.10.83 | Caorso | IT, AMN | Core instability during special tests
17.10.84 | S. Maria de Garona | ES, GE | Power oscillations during operation
23.02.87 | TVO 1 | Fe, ABB | Power oscillations during plant start up
09.03.88 | La Salle 2 | US, GE | Core instability with scram caused by neutron flux oscillation
29.10.88 | Vermont Yankee | US, GE | Power oscillations
26.10.89 | Ringhals 1 | SE, GE | Instability during power ascent after refueling
08.01.89 | Oskarshamn | SE, ABB | Power oscillations
29.01.91 | Cofrentes | ES, GE | Power oscillations due to inadvertent entry in the reactor power-core flow map instability zone “B”
03.07.91 | Isar 1 | DE, KWU | Scram due to power oscillations
15.08.92 | WNP | US, GE | Power oscillations
09.07.93 | Perry | US, GE | Entry into a region of core instability
17.07.96 | Forsmark 1 | SE, ABB | Local oscillations due to a bad seated fuel assembly
08.02.98 | Oskarshamn 3 | SE, ABB | Power oscillations due to a bad combination of core design and control-rod pattern during start up
25.02.99 | Oskarshamn 2 | SE, ABB | Power oscillations after a turbine trip with pump runback
Notes: The power-flow stability related to thermal-hydraulic and thermal-nuclear coupled instabilities is one of the important technology gaps identified by Gen-IV roadmap, and needs to be investigated thoroughly.

## Slide 4: Objectives
Develop a frequency domain linear stability analysis code for SCWR
  Thermal-hydraulics model
  Nuclear kinetics model
  Fuel heat transfer model
Investigate the power-flow instability phenomena in SCWR
  Understand instability phenomena in SCWR
  Identify important variables and their stable domains
  Assess the adequacy of conventional stability analysis methods and determine the need for advanced tools/models
Perform parametric studies and identify stable domains
Notes: The objective of this project is to investigate the power-flow instability phenomena in SCWR by frequency linear analysis in order to understand the instability phenomena in SCWR better, identify important variables and their stable domains, assess the adequacy of conventional stability analysis methods and determine the need for advanced tools/models.
To achieve the objectives, it is planned to review various proposed concepts of SCWRs and the stability analysis methods for boiling water reactors (BWRs), for which thermal-hydraulic and coupled thermal-nuclear instabilities are important design concerns.
Based on these review results, we will develop a linear stability analysis code by incorporating simplified core thermal-hydraulic model, nuclear kinetics model, and fuel heat transfer model. A linear approximation of the nonlinear coupled equations will be developed and the transfer function will be evaluated.
Stability analysis will be performed under various assumptions about input perturbations.
The sensitivity analysis studies will consider the effects of important variables, such as nonuniformity of power distribution and water density, fuel temperature feedback coefficients, fuel rod thermal characteristics, coolant channel hydraulic characteristics, inlet and exit restrictions, heat transfer phenomena, and core boundary conditions.

## Slide 5: Computational Models
Thermal Hydraulics Model
  Single-channel mass, momentum, and energy conservation equations
    No model for heat transfer to water rods
  Finite difference scheme for axial nodalization
    Iterative solution scheme for given inlet flow rate, temperature and outlet pressure
  NIST/ASME STEAM package released in 1997
Nuclear Kinetics Model
  Point kinetics model with six delayed neutron groups
    No capability for regional (out-of-phase) instability study
  Doppler and coolant density feedback
Notes: Up to now, we review the proposed SCWR concepts and BWR stability analysis methods and initiate the frequency domain linear analysis code development.

## Slide 6: Computational Models
Fuel Heat Transfer Model
  One-dimensional heat conduction equation
    No axial or azimuthal heat conduction
    Temperature-dependent heat conductivities
  Finite difference scheme for radial nodalization
    Iterative solution scheme based on thermal conductivity updates
Frequency Domain Linear Analysis
  Linearization of governing equations around steady state condition and subsequent Laplace transformation of linearized equations
  Direct search scheme based on modified Newton’s method for dominant root of system characteristic equation
  Decay ratio =
Notes: Up to now, we review the proposed SCWR concepts and BWR stability analysis methods and initiate the frequency domain linear analysis code development.

## Slide 7: US Gen-IV SCWR Reference Design
SCWR Fuel Assembly Design
Thermal power | 3022 MW
Electric power | 1315 MW
Thermal efficiency | 43.5%
Operating pressure | 25 MPa
Reactor inlet/outlet temperature | 280/500C
Reactor flow rate | 1561 kg/s
Fuel pin OD | 10.2 mm
Fuel pin pitch | 11.2 mm
Cladding thickness | 0.63 mm
Cladding materials | ODS steel
Fuel pellet OD | 8.94 mm
Fuel composition | UO2, 95% TD
Fuel enrichment | 5% wt. average
Heated length | 4.27 m
Fission gas plenum length | 0.39 m
Total fuel pin height | 4.66 m
Fill gas pressure at room temperature | 3.0 MPa

## Slide 8: Preliminary Results
Decay Ratio of Thermal-Hydraulic Stability (ζ=0.01)
Unstable only when power-to-flow ratio is greater than ~1.2
Potential instability during start-up
Careful start-up procedure is required

## Slide 9: Preliminary Results
Decay Ratio of Thermal-Hydraulic Stability
Inlet orifice improves SCWR stability significantly
Normal operating points in power and core flow tend to be very stable
ζ=0.01
ζ=5.0

## Slide 10: Preliminary Results
Due to separate water rods, SCWR coolant density coefficient is substantially smaller than BWR
Because of higher enrichment, SCWR fuel temperature coefficient is somewhat smaller than BWR
Thermal-nuclear coupled stability would be better than BWR

## Slide 11: Summary and Future Work
Frequency domain linear stability analysis code for SCWR is being developed
  Basic programming has been completed
  Thermal-nuclear coupled program is being debugged
Preliminary results for US SCWR reference design showed:
  Thermal-hydraulic stability seems to be better than BWR
  Thermal-nuclear coupled stability could be better than BWR
Perform parametric studies and identify stable power-flow domains
  Thermal-nuclear coupled stability analyses
  Sensitivity analyses
Improvements of computation models
  Multiple channel thermal-hydraulic model
  Space-dependent kinetics model
Notes: Up to now, we review the proposed SCWR concepts and BWR stability analysis methods and initiate the frequency domain linear analysis code development.